## Slide 1
Electrical and Electronic Engineering Principles 2
Mohammad Hosseinabady
mohammad.hosseinabady@kaplan.com
UWEBIC IY425
Thursday 20-Jan-2022
Capacitors

## Slide 2: Today Topics

## Slide 3: Reference
Chapter 9 & 10
Electronics Fundamentals Circuits, Devices and Applications
Thomas L. Floyd David L. Buchla Eighth Edition

## Slide 4: Capacitor (reminder)
A capacitor is a passive electrical component.
It stores electrical charge and has the property of capacitance.
Conductive Plates
Connecting Leads
Dielectric
C
Circuit Symbol

## Slide 5: Capacitor (for study)
a dielectric (or dielectric material or dielectric medium) is an electrical insulator that can be polarised by an applied electric field. When a dielectric material is placed in an electric field, electric charges do not flow through the material as they do in an electrical conductor, because they have no loosely bound, or free, electrons that may drift through the material, but instead they shift, only slightly, from their average equilibrium positions, causing dielectric polarisation.
dielectric
conductive
A conductive substance allows heat or electricity to travel through it

## Slide 6: Homework (reminder)
Conductive Plates
Dielectric
-
+
-
-
-
+
+
+
1- How does a capacitor store charge?
2- How does a capacitor store energy?
Hint: Chapter 9 Capacitors in the course textbook.

## Slide 7: Leakage (reminder)
No insulating material is perfect.
The dielectric of any capacitor will conduct some very small amount of current.
Thus, the charge on a capacitor will eventually leak off.
Some types of capacitors have higher leakages than others.
An equivalent circuit for a nonideal capacitor is shown in this Figure.
The parallel resistor represents the extremely high resistance (several
hundred or more) of the dielectric material through which there is leakage current.
None-ideal Capacitor

## Slide 8: Capacitance (reminder)
C
Circuit Symbol
The amount of charge that a capacitor can store per unit of voltage across its plates.
Capacitance
Charge
Voltage
Capacitance

## Slide 9: Capacitance (reminder)
C
Circuit Symbol
Coulomb
Volt
Farad
Most capacitors that are used in electronics work have capacitance values in microfarads () and picofarads ().

## Slide 10: Capacitance (reminder)
C
Circuit Symbol
A microfarad is one-millionth of a farad:
A picofarad is one-trillionth of a farad:

## Slide 11: Capacitance – Unit Conversion (reminder)

## Slide 12: Example
A certain capacitor stores 50 microcoulombs () when 10 V are applied across its plates. What is its capacitance?

## Slide 13: Example
A capacitor has across its plates. How much charge does it store?

## Slide 14: Example
Convert the following values to microfarads:

## Slide 15: Series Capacitors (reminder)

## Slide 16: Example (reminder)
Find the voltage across each capacitor:

## Slide 17: Parallel Capacitors (reminder)

## Slide 18: Capacitor in DC Current (reminder)
+
-
+
-
s
time
Ideal capacitor

## Slide 19: Capacitor in DC Current (reminder)
+
-
+
-
s
time
In Practice
When a capacitor charges or discharges through a resistance, a certain time is required for the capacitor to charge fully or discharge fully.
The time constant of a series RC circuit determines the rate at which the capacitor charges or discharges.

## Slide 20: Example (reminder)
A series RC circuit has a resistance of and a capacitance of .
What is the time constant?

## Slide 21: Capacitor in DC Current (reminder)
+
-
+
-
s
time
Charging
Discharging
Charging from 0:
Discharging to 0:

## Slide 22: Capacitor in DC Current (reminder)
Exponential voltage curves for the charging and discharging of a capacitor in an RC circuit.

## Slide 23: Example
How long does it take to fully charge the capacitor?

## Slide 24: Capacitor in DC Current

## Slide 25: Example
Write the charging and discharging formulations for this circuit.

## Slide 26: Capacitor in AC
+
-
~
Circuit in Multisim
Voltage: blue
Current: Green

## Slide 27: Sine Wave – Period (reminder)
Positive maximum
Negative maximum
Time (t)
Voltage or Current
T: period
A cycle

## Slide 28: Sine Wave – Frequency (reminder)
Lower frequency: fewer cycles per second
Higher frequency: more cycles per second

## Slide 29: Sine Wave – Values (reminder)
Peak Value
: The peak value of a sine wave is the value of voltage (or current) at the positive or the negative maximum (peaks) with respect to zero.
Peak-to-Peak Value
RMS Value
The term rms stands for root mean square.
The rms value, also referred to as the effective
value, of a sinusoidal voltage is actually a measure of the heating effect of the sine wave.

## Slide 30: Capacitor in AC
+
-
~
Voltage
Current

## Slide 31: Capacitor in AC
+
-
~
Capacitive Reactance
Unit: Ohm

## Slide 32: Example
A sinusoidal voltage is applied to a capacitor, as shown in this figure. The frequency of the sine wave is
Determine the capacitive reactance.
+
-
~

## Slide 33: Quiz
Determine the frequency required to make the capacitive reactance in this figure equal to
=
+
-
~
3.39 kHz
Answer

## Slide 34: Reactance for Series Capacitors

## Slide 35: Reactance for Parallel Capacitors

## Slide 36: Example
What is the total capacitive reactance in each circuit in this figure?

## Slide 37: Example
=
+
-
~
Determine the rms current in this figure.

## Slide 38: Quiz
=
+
-
~
Determine the rms current in this figure.

## Slide 39: Capacitive Voltage Divider
~

## Slide 40: Example
What is the voltage across C2 in the circuit?

## Slide 41: RC Circuit
~
In a series RC circuit, the current is the same through both the resistor and the capacitor.
Thus, the resistor voltage is in phase with the current, and the capacitor voltage
lags the current by .Therefore, there is a phase difference of between the resistor
voltage, and the capacitor voltage.

## Slide 42: RC Circuit
~
You know from Kirchhoff’s voltage law that the sum of the voltage drops must equal the source voltage. However, since and are out of phase with each other, they must be added as phasor quantities, with

## Slide 43: Example
~
Determine the source voltage and the phase angle in this figure. Draw the voltage phasor diagram.
5

## Slide 44: Impedance
~
~

## Slide 45: Example
~
~
Determine the impedance and the phase angle of the RC circuit in this figure. Draw the impedance triangle.