## Slide 1: Electrical and Electronic Engineering Principles 1
Mohammad Hosseinabady
UWEBIC IY424
mohammad@highlevel-synthesis.com

## Slide 2: Today’s Topics

## Slide 3: Reference
Chapter 2 of
Electronics Fundamentals Circuits, Devices and Applications Thomas L. Floyd David L. Buchla Eighth Edition

## Slide 4: Find the Book in the UWE Library
https://uwe.summon.serialssolutions.com/search?q=electronics+fundementals#!/search?ho=t&l=en-UK&q=electronics%20fundementals

## Slide 5: Voltage
Voltage is defined as energy per unit of charge and is expressed as
Voltage in volts (V)
Energy in joules (J)
Charge in coulombs (C)

## Slide 6: Example
If of energy are required to move of charge, what is the voltage?
How much energy is required to move 50 C from one point in a circuit to another
when the voltage between the two points is 12 V?
Answer:

## Slide 7: DC Voltage Source
A voltage source provides electrical energy.
+
-
An ideal voltage source can provide a constant voltage
for any current required by a circuit.
Voltage Source
DC
AC

## Slide 8: DC Voltage Source
Types of DC Voltage Sources
Batteries
Fuel Cells
Solar Cells
Generators
The Power Supply
Thermocouple
Piezoelectric Sensors

## Slide 9: Current
Voltage provides energy to electrons that allows them to move through a circuit. This movement of electrons is the current
Current in a conductive material is measured by the number of electrons (amount of charge) that flow past a point in a unit of time.
Current in amperes (A)
Charge of electrons in coulombs (C)
Time in second

## Slide 10: Example
Ten coulombs of charge flow past a given point in a wire in . What is the current in amperes?
If there are of direct current through the filament of a light bulb, how many
coulombs have moved through the filament in 1.5 s?
Answer:

## Slide 11: Current Source
An ideal current source can provide a constant current in any load.
Symbol

## Slide 12: Resistance
When there is current through a material, the free electrons move through the material and occasionally collide with atoms.
These collisions cause the electrons to lose some of their energy, and thus their movement is restricted.
The more collisions, the more the flow of electrons is restricted.
This restriction varies and is determined by the type of material.
The property of a material that restricts the flow of electrons is called resistance, designated with an R.
Atoms
Electrons

## Slide 13: Resistance
Resistance/Resistor
Schematic Symbol
R
Unit of resistance: ohm
The reciprocal of resistance is conductance: G.
Example:
The unit of conductance is the siemens: S

## Slide 14: Resistors
Components that are specifically designed to have a certain amount of resistance.
Resistors

## Slide 15: Four Bands Colour Coded Resistors
Resistors
1st digit
2nd digit
multiplier (number of zeros following the 2nd digit)
tolerance

## Slide 16: Example
Find the resistance value in ohms and the percent tolerance for this colour-coded resistors.
  First band is red 2
  Second band is violet 7
  Third band is orange 3 zeros,
  Fourth band is silver tolerance.

## Slide 17: Quiz
Find the resistance value in ohms and the percent tolerance for this colour-coded resistors.
First band is brown 1,
Second band is black 0,
Third band is brown 1 zero,
Fourth band is silver 10% tolerance.

## Slide 18: Quiz
Find the resistance value in ohms and the percent tolerance for this colour-coded resistors.
First band is green 5,
Second band is blue 6,
Third band is green 5 zeros,
Fourth band is gold 5% tolerance.

## Slide 19: Five Bands Colour Coded Resistors
Resistors
1st digit
2nd digit
Multiplier (number of zeros following the 3rd digit)
tolerance
3rd digit

## Slide 20: Five Bands Colour Coded Resistors
 | DIGIT | Colour
First band—1st digit Second band—2nd digit Third band—3rd digit | 0 | Black
 | 1 | Brown
 | 2 | Red
 | 3 | Orange
 | 4 | Yellow
 | 5 | Green
 | 6 | Blue
 | 7 | Violet
 | 8 | Gray
 | 9 | White
Fourth band—multiplier | 0.1 | Gold
 | 0.01 | Silver
Fifth band—tolerance |  | Red
 |  | Brown
 |  | Green
 |  | Blue
 |  | Violet
 | DIGIT | Colour
First band—1st digit Second band—2nd digit Third band—3rd digit | 0 | Black
 | 1 | Brown
 | 2 | Red
 | 3 | Orange
 | 4 | Yellow
 | 5 | Green
 | 6 | Blue
 | 7 | Violet
 | 8 | Gray
 | 9 | White
Fourth band—multiplier | 0.1 | Gold
 | 0.01 | Silver
Fifth band—tolerance |  | Red
 |  | Brown
 |  | Green
 |  | Blue
 |  | Violet
First band is red 2,
Second band is violet 7,
Third band is black 0,
Fourth band is gold 0.1,
Fifth band is red 2% tolerance.

## Slide 21: Quiz
 | DIGIT | Colour
First band—1st digit Second band—2nd digit Third band—3rd digit | 0 | Black
 | 1 | Brown
 | 2 | Red
 | 3 | Orange
 | 4 | Yellow
 | 5 | Green
 | 6 | Blue
 | 7 | Violet
 | 8 | Gray
 | 9 | White
Fourth band—multiplier | 0.1 | Gold
 | 0.01 | Silver
Fifth band—tolerance |  | Red
 |  | Brown
 |  | Green
 |  | Blue
 |  | Violet
 | DIGIT | Colour
First band—1st digit Second band—2nd digit Third band—3rd digit | 0 | Black
 | 1 | Brown
 | 2 | Red
 | 3 | Orange
 | 4 | Yellow
 | 5 | Green
 | 6 | Blue
 | 7 | Violet
 | 8 | Gray
 | 9 | White
Fourth band—multiplier | 0.1 | Gold
 | 0.01 | Silver
Fifth band—tolerance |  | Red
 |  | Brown
 |  | Green
 |  | Blue
 |  | Violet
First band is yellow 4,
Second band is black 0,
Third band is red 2,
Fourth band is black 0,
Fifth band is brown 1% tolerance.

## Slide 22: Resistor Label Codes
surface-mount resistors
R: a multiplier of 1 (no zeros after the digits),
K: a multiplier of 1000 (three zeros after the digits),
M: a multiplier of 1,000,000

## Slide 23: Quiz
Interpret the following alphanumeric resistor labels:
470
5R6
68K
10M
3M3
470 = 470
5R6 = 5.6
68K = 68
(d) 10M = 10
(e) 3M3 = 3.3
Answer

## Slide 24: Variable Resistors
1
2
3
1
2
1
2
3
Potentiometer
Rheostat
used to divide voltage
used to control current
Potentiometer connected
as a rheostat
https://www.youtube.com/watch?v=D4DjJDKO6IQ

## Slide 25: Example
1
2
3

## Slide 26: Variable Resistance Sensors
Thermistors
Photoconductive cell
Strain gauge
resistance as a function of temperature
resistance as a function of light
resistance as a function of force
Search on google and YouTube for resistance sensors

## Slide 27: ELECTRIC CIRCUIT

## Slide 28: Multisim Simulator
https://www.multisim.com/
https://www.youtube.com/watch?v=gBhlr2AcaR0
A useful tutorial:

## Slide 29: Switch
DPST:
Double-pole–single-throw
SPDT:
Double-pole–double-throw
PB:
Push-button

## Slide 30: Ground
Ground is the reference point in an electric circuit.
Voltages are always specified with respect to another point.

## Slide 31: BASIC CIRCUIT MEASUREMENTS
In working on electrical or electronic circuits, you will frequently need to measure voltage, current, and resistance.
Voltmeter
The instrument used to measure voltage
Ammeter
The instrument used to measure current
Ohmmeter
The instrument used to measure resistance

## Slide 32: Portable Multimeters
Digital multimeter
Analog multimeter

## Slide 33: Measuring Current
A
+
-
+
-
+
-
series connection

## Slide 34: Measuring Voltage
V
+
-
+
-
+
-
parallel connection

## Slide 35: Measuring Resistance
To measure resistance, connect an ohmmeter across the resistor.
The resistor must first be removed or disconnected from the circuit.

## Slide 36: Digital Multimeters (DMMs)
https://www.youtube.com/watch?v=grDoGiSxOP0

## Slide 37: Analog Multimeters (DMMs)
https://www.youtube.com/watch?v=9rGDx92McTY

## Slide 38: Quiz
+
-
V1
+
-
V2
+
-
SW
1
2
SW  1
SW  2
V1=0
V2=5
5v
V2=5
V1=0

## Slide 39: Quiz
Build this circuit in MultisimOnline and simulate that.

## Slide 40: Quiz
1- A resistor color coded with brown, black, and orange bands has a value of .
Answer: True
2- A normally open push-button switch can carry current when not pushed.
Answer: False

## Slide 41: Quiz
Show the placement of an ammeter and a voltmeter to measure the current and the voltage on R1.
+
-